## Slide 1: What is the cost of disregarding market feedback in transmission expansion planning?
Isaac-Camilo Gonzalez Romero1, Sonja Wogrin1, Tomás Gómez1
1 Universidad Pontificia Comillas, Instituto de Investigación Tecnológica (IIT), Madrid, Spain
*

## Slide 2
TEP
GEP
Generation Expansion Planning and Transmission Expansion Planning
Proactive

## Slide 3: Generation and Transmission Expansion Planning
TSO (TEP)
Deregulated market
GENCOs (GEP)

## Slide 4: Research Question
If instead of assuming a traditional cost minimization approach, a TSO foresees strategic market outcomes, can this be beneficial for society?
What can be the results of considering distinctive policy objectives?

## Slide 5: Mathematical Formulation

## Slide 6: Centralized Planning (CP)
Minimizes Total Cost
Decision Variables:
Binary transmission expansion
Continuous generation expansion
Operation Variables
Assumptions:
Inelastic Demand
Perfect Competition
Perfect Information
Single Optimization Problem
Notes: jhfhh

## Slide 7: Bilevel Proactive Equilibrium (BP)
GENCOs can behave both Perfectly Competitive (PC) or Cournot Oligopoly (CO)
TSO or social planner (decides TEP)
1) Min Cost (CM-BP)
2) Max Welfare (WM-BP)
GENCOs
(decide GEP and operation)
Maximize Benefits
Market Clearing Condition
SO
(decides flows)
Maximizes Congestion Rents
Upper Level
Lower
Level
Consumers
(decide demand)
Maximize Demand Utility
Notes: jhfhh

## Slide 8: MIP Reformulaiton
Objective Function:
Max Welfare / Min Cost
Subject to:
Dual Feasibility Constraints
Complementarity Constraints
Primal Feasibility Constraints
  product & consumption limits
  spillage & reservoir limits
  reservoir balance
  wind availability limits
  line capacities, DC flow
  positive demand
MIP linearization
Disjunctive Constraints
Upper Level
Lower Level
KKT Conditions
    Market Clearing Condition

## Slide 9: Linked Representative Periods
Chart: 
Hourly Year Demand
Representative Days
RP1
RP2
RP3
RP4
D. A. Tejada-Arango, M. Domeshek, S. Wogrin, and E. Centeno, “Enhanced Representative Days and System States Modeling for Energy Storage Investment Analysis,” IEEE Trans. Power Syst., vol. 8950, no. c, pp. 1–1, 2018.

## Slide 10: Storage Representation
Intraday constraints
Interday constraints
D. A. Tejada-Arango, M. Domeshek, S. Wogrin, and E. Centeno, “Enhanced Representative Days and System States Modeling for Energy Storage Investment Analysis,” IEEE Trans. Power Syst., vol. 8950, no. c, pp. 1–1, 2018.

## Slide 11: CASE STUDY

## Slide 12: Input Data
1
2
3
4
5
6
Chart: 
 | 0.54478 | 0.47925 | 0.43564 | 0.41501 | 0.40338 | 0.41054 | 0.47758 | 0.53699 | 0.60073 | 0.66608 | 0.72949 | 0.77659 | 0.80519 | 0.81455 | 0.79219 | 0.767 | 0.76489 | 0.77782 | 0.77111 | 0.75043 | 0.74948 | 0.81087 | 0.77218 | 0.68881 | 0.55069 | 0.49018 | 0.44827 | 0.42743 | 0.41683 | 0.44423 | 0.55172 | 0.68834 | 0.77474 | 0.81369 | 0.8454 | 0.85468 | 0.86073 | 0.85405 | 0.79992 | 0.79899 | 0.80075 | 0.82178 | 0.89916 | 0.93282 | 0.92204 | 0.87637 | 0.78568 | 0.73427
Six-Node System
5 existing lines
5 existing generation units
  CCGT
  Coal
  Nuclear
  Hydro
  Battery
1 candidate generator
  CCGT
Time Scope: 1 year
2 representative days
168 hours window
Deterministic Case
Elastic Demand

## Slide 13: Cases
vs
vs
Policy Objectives
CM-BP
WM-BP
Regret
CP
BP

## Slide 14: RESULTS

## Slide 15: Distinctive Policy Objectives Economic Results
 | Units | CM |  | WM
TEP | Lines | 6_1/6_3 | < | ALL
GEP | MW | 437.6 | > | 410.3
Welfare | (M€) | 1758.4 | < | 1896
Total Cost | (M€) | 367.5 | < | 440
Total Demand | (TWh) | 253.2 | < | 278
We consider Perfect Competition in the lower level
1
2
3
4
5
6
(112.2) [114.1]
(138) [127]
(35.6) [32.7]
(274) [168]
(54) [54]
(15) [15]

## Slide 16
Distinctive Policy Objectives Planning and Prices
Reservoir Level
Weeks
Hourly Prices

## Slide 17: Regret Computation
Bilevel Proactive Cost Min
Elastic Demand- Cournot
BP
Centralized Planning Inelastic Demand Perfect Comp
“Naïve CP”
Demand
Lower Level Problem
Elastic Demand - Cournot
“Actual CP”
TEP
Regret = Actual CP – BP

## Slide 18: Regret Results
 | Units | BP | Naïve CP | Actual CP
TEP | Lines | 6-3 | 6-1/6-3 | 6-1/6-3
GEP | MW | 214.8 | 220.9 | 214.2
Welfare | M€ | 809.2 | 587 | 809.2
Total Cost | M€ | 225.9 | 131.8 | 235.6
Total Demand | TWh | 119.3 | 119.3 | 119.4
Regret | M€ |  |  | 9.8
Relative Regret | M€/TWh |  |  | 0.08
Cost Regret = 4%
Welfare Regret = 0%
No Regret with perfect competition

## Slide 19: CONCLUSIONS
Distinctive policy objectives can result in different equilibria even if the market is perfectly competitive.
Disregarding strategic market feedback can result in sub-optimal planning results that lead to higher total cost or lower welfare.

## Slide 20: REFERENCES
[1] P. Pisciella, M. Bertocchi, and M. T. Vespucci, “A leader-followers model of power transmission capacity expansion in a market driven environment,” Comput. Manag. Sci., vol. 13, no. 1, pp. 87–118, 2016.
[2] D. A. Tejada-Arango, M. Domeshek, S. Wogrin, and E. Centeno, “Enhanced Representative Days and System States Modeling for Energy Storage Investment Analysis,” IEEE Trans. Power Syst., vol. 8950, no. c, pp. 1–1, 2018.
[3] S. Jin, S. M. Ryan, and A. Sets, “A Tri-Level Model of Centralized Transmission and Decentralized Generation Expansion Planning for an Electricity Market — Part I,” vol. 29, no. 1, pp. 132–141, 2014.
[4] S. K. K. Ng, J. Zhong, and C. W. Lee, “A Game-Theoretic Study of the Strategic Interaction between Generation and Transmission Expansion Planning,” 2009 IEEE/PES Power Syst. Conf. Expo., pp. 1–10, 2009.
[5] D. Pozo, J. Contreras, and E. Sauma, “If you build it, he will come: Anticipative power transmission planning,” Energy Econ., vol. 36, pp. 135–146, 2013.
[6] S. You, S. W. Hadley, M. Shankar, and Y. Liu, “Co-optimizing generation and transmission expansion with wind power in large-scale power grids—Implementation in the US Eastern Interconnection,” Electr. Power Syst. Res., vol. 133, pp. 209–218, 2016.

## Slide 21
This work was supported by Project Grant ENE2016-79517-R, awarded by the Spanish Ministerio de Economía, Industria y Competitividad.
https://stexem.iit.comillas.edu/
Questions